## Slide 2
ms-dos demoscene :: distinctive periods
Original IBM PC machines
??????????????????
the birth (1990 – 1992)
286-386, EGA/VGA, Covox/SB
the golden age (1993 – 1996)
486, VGA, GUS
the transfiguration (1997 – 1999)
Pentium, SVGA, GUS/SB16

## Slide 3
ms-dos demoscene :: the birth :: 1990
inspired by both cracktros and Amiga demoscene, started from simple EGA/VGA experiments with ripped samples and 4 channel mods.
Slideshow by Future Crew (1990) – first ever production with 4-channel MOD music
Megademo by The Space Pigs (1990) – the first big scene production, and it runs on EGA!
Scream Tracker 2 by Future Crew (1990-1992) – marking the start of PC trackers era

## Slide 4
ms-dos demoscene :: the birth:: 1991
…slowly drifting towards complex vector worlds ….
Vicky by The Space Pigs (1991)
Cronologia by Cascada (1991)
VectorDemo by Ultraforce (1991)

## Slide 5
ms-dos demoscene :: the birth :: 1992
eventually reaching Amiga level of complexity with rapid performance growth
Unreal by Future Crew (1992)
Amnesia by Renaissance (1992)
Assembly 1992 – the first major demoparty with PC compos

## Slide 6
ms-dos demoscene :: the birth :: 1993
... and driving beyond four channel MODs with new trackers and hardware like GUS …
Second Reality by Future Crew (1993)
Crystal Dream II by Triton (1993)
Untitled by Dust (1993)

## Slide 7
ms-dos demoscene :: the golden age:: 1994
... quickly catching up with and beyond the new Amiga AGA capabilities …
Verses by Electromotive Force (1994)
No! by NoooN (1994)
Cyboman 2 by Complex (1994)

## Slide 8
ms-dos demoscene :: the golden age:: 1995
... expanding to high resolution and phong shaded duck.3ds land …
Caero by Electromotive Force (1995)
Stars: Wonders of the World by NoooN (1995)
Drift by Wild Light (1995)

## Slide 9
ms-dos demoscene :: the golden age:: 1996
Toasted by Cubic Team & $een (1996)
Inside by CNCD (1996)
Contrast by Oxygene (1996)
... sqeezing last bits from freedirs and lens flares …

## Slide 10
ms-dos demoscene :: the transfiguration :: 1997
Boost by Doomsday (1997)
Square by Pulse (1997)
Stash by The Black Lotus (1997)
... getting backed by Pentium and High Color …

## Slide 11
ms-dos demoscene :: the transfiguration :: 1998
te-2rb by TPOLM (1998)
Kkowboy by Blasphemy & Purple (1998)
State of Mind by Bomb (1998)
... quickly moving towards design in lieu of code …

## Slide 12
ms-dos demoscene :: the transfiguration :: 1999
bakkslide 7 by Hellcore & Omnicolour (1999)
Discloned by Haujobb (1999)
moralhardcandy by Blasphemy (1999)
... and finally transformating to world of Windows …

## Slide 13
ms-dos demoscene :: current state
during 1999-2000, the PC scene almost entirely moved on Windows, exploring new 3D accelerated horizons, running towards more polygons and shaders….
but in recent 10 years with a strong retroscene movement pushing from above, the DOS scene starts to resurrect (or kinda?...)

## Slide 14
ms-dos demoscene :: current state
exploring both platfoms known for so many years…
...and squeezing last bits from ancient PCs
8088 MPH by Hornet & CRTC & Desire (2015)
cöncept by Ümlaüt Design (2021)
Rave On by Satori & da Jormas (2018)

## Slide 15
ms-dos demoscene :: current state
… as well as packing visuals to as many bytes as you can

## Slide 16
graphics cards :: mda/hercules
MDA introduced with the first IBM PC in 1981
based on Motorola MC6845 CRTC
supports only monochrome 80x25 textmode with 9x14 charset -> 720x350 resolution at 50 Hz
included parallel port at 0x3BC
4kB of VRAM at 0xB0000
Later, Hercules released HCG with monochrome graphics mode, backwards compatible with MDA hardware/software
720x348 pixels, stored as 4-line interleaved bitmap due to 6845 limitations
64 kB of VRAM, with 2nd page at 0xB8000 (
cheap HGC cards were popular as both low-cost business and dual-head soultion for software debugging

## Slide 17
graphics cards :: cga
along with MDS, Color Graphics Adapter was also released
also based on Motorola MC6845 CRTC
supports 40x25 and 80x25 text modes with 8x8 matrix
16kB of VRAM at 0xB8000

## Slide 18: hardware :: sound devices
originally PC has never been a multimedia machine
but as PC install base quickly went beyond corporate and office, growing CPU power became appealing for entertainment uses

## Slide 19
sound devices :: pc speaker
the most distinctive and ubiquitous PC sound device :)
supported all the way from first IBM PC to recent machines, and literally by every PC OS
originally used for system diagnostics and simple beeps, later being “enhanced” to digitized PWM samples and multichannel music
from hardware side, it’s basically:
1-bit output from PIT Channel 2…
ANDed with port 0x61 bit 0 (+ PIT gate @ bit 1)
but let alone PWM, the square wavy nature of sounds and one channel is more than enough!
(check System Beeps musicdisk and 8088MPH, also Monotone tracker
PC Speaker on original IBM PC 5150 (image by PixelatedArcade)

## Slide 20
sound devices :: pc speaker :: realsound
with a bit of trickery (Ch2 in Mode 0 + IRQ0 at sample rate), an aprx. 5-6 bit PWM sample playback is possible
cons: IRQ0 eats CPU time, audible squeak at sample rate, audio quality degrades with sample rate increase (20 KHz is realistic limit, giving 50 levels – almost 6 bits)
widely supported by software, incl. majority of DOS trackers and module players (ST2/FT2/IT), as well as by early DOS demos and games (known as RealSound)

## Slide 21
sound devices :: covox
a totally simple and cheap DIY 8-bit DAC for parallel port
originally introduced in 1987 as Covox Speech Thing, become widespread as DIY device
provides full 8-bit sample resolution, (depends on DAC accuracy but still generally better than PC Speaker)
enhanced versions (stereo on one/two LPT ports, DAC ICs, filters and amplifiers, ADC capability, ISA cards, etc)
adapted and further enhanced for almost every 8/16-bit platform (Amstrad CPC, ZX Spectrum, MSX, etc)
enhanced variant known as Disney Sound Source added 16-byte FIFO and built-in loudspeaker, partially compatible with original Covox but has own diffirences

## Slide 22
sound devices :: covox :: build it yourself!

## Slide 23
sound devices :: covox :: example and notes
speaking of trackers/players/demos - almost every software supporting PC Speaker in RealSound mode supports Covox also. handles up to 44/48 KHz pretty well
stereo modes are different story, though – at least 3 incompatible Stereo-on-one-LPT protocols + two-port variant.
Covox Inc. also supplied digital sound drivers for Windows 3.x, although not much stable

## Slide 24
sound devices :: opl2/3
Yamaha YM3812 OPL2 FM synthesizer, introduced to PC with Adlib Music Synthesizer card in 1987
9 two-operator FM channels + percussion mode
4 waveforms, mono out
no PCM output capability, although it’s possible to get logarithmic 6bit DAC via FM operator tricks
easy to program, requires long delays between register writes (doesn’t matter much for XT, but becomes cumbersome on 286 and faster)
supported by most ISA soundcards (popularized by original Sound Blaster, two OPL2 in SB Pro)
supported by majority of DOS games, frequently used in BBS intros and cracktros

## Slide 25
sound devices :: opl2/3
later YMF282 (used in SB Pro 2/16 and Adlib Gold) is backwards software compatible with OPL2
18 2-OP or 6 2-OP + 6 4-OP FM channels, stereo capability, 4 new waveforms
reduced access delays
many later ISA sound chips implement custom OPL3 compatible cores (Creative CQM, ESFM, etc.), with varying sound faithfulness to the original OPL3
most OPL trackers supports OPL2 feature level (HSC, RAD, AMusic, Scream Tracker 3), others like Adlib Tracker support OPL3 features
Adlib Tracker II

## Slide 26
sound devices :: sound blaster
released in 1989, introduced DMA PCM to PC market
bundles OPL2 for Adlib Compatibility + two SAA1099, “DSP” chip (relabeled Intel 8051 MCU) handles PCM playback/recording + ADPCM playback + MIDI
originally supported max. 23 kHz 8 bit mono, later SB 2.0 added auto-init DMA capability for buffered playback + hi-speed mode for 44 kHz audio
relatively easy to program, supports DMA/IRQ for CPU offloading
quickly become a market success, supported by many DOS games, demos are quite different story though

## Slide 27
sound devices :: sound blaster pro/16
SB Pro finally added stereo PCM + OPL playback
max 22 kHz 8 bit stereo or 44 kHz 8 bit mono
de-facto standard across ISA soundcards, often enhanced with own extensions (ESS cards)
later SB Pro 2.0 uses single OPL3 instead of two OPL2
SB 16 introduced 16-bit CD-quality PCM + MPU-401 compatible MIDI interface
44 kHz 16 bit stereo, backwards compatible with SB 2.0 but not SB Pro’s stereo mode
games rarely take advantage of 16-bit capabilities, but many trackers/demos/players support SB16 for better sound quality (still rarely can beat the GUS :)

## Slide 28
sound devices :: gravis ultrasound
the DOS demoscene golden standard :)
released in 1992, used GF1 chip + onboard RAM for wavetable synthesis and sample playback
32 wavetable channels with linear interpolation, volume, pitch and panning control, up to 44 kHz 16 bit hardware mixing (full 32ch is 19 kHz though)
up to 1 MB of onboard RAM, 8/16bit samples
No Adlib/SB compatibility, PCM streaming has to be done by free wavetable channel + DMA
very easy to program – ideal for tracked music
almost all post-1993 demos support GUS (often as sole sound device), as well as trackers and players

## Slide 29
sound devices :: gravis ultrasound :: max/pnp
GUS MAX bundled CS4231A codec for streamed PCM capability and better SB emulation
in 1995, AMD develops Interwave IC, used in GUS PnP and several 3rd party cards
full 32 channels at 44 kHz + MPU-401 MIDI
up to 16 MB of sample RAM (upgradeable with 30-pin SIMMs) + 1 MB ROM
backwards compatible with GF1
some demos/players support Interwave natively, other will work fine in classic GUS mode

## Slide 30
sound devices :: sound blaster awe32/64
basically SB16 + EMU8000 wavetable synthesizer
32 wavetable channels with 4-point interpolation, volume, pitch and panning control, up to 44 kHz 16 bit mixing + resonant filters + effect processing
16-bit only always-looped samples, up to 28 MB RAM + 1 MB ROM
Creative originally didn’t disclosed register details, several people reverse engineered EMU8000 internals then finally official hardware reference has been released
needs complex init compared with GUS, wavetable limitations (max 176 kHz pitch, 16 bit samples, etc.)
not as common as GUS, supported by some trackers (e.g. IT2) and demos

## Slide 31
sound devices :: midi
originally used for music equipment control
1984 – Roland MPU-401 – universal MIDI interface, supports many platforms, incl. PC, support UART and intelligent accelerated mode
1987 – Roland MT32/LAPC-1 – reference music synth for early DOS games
1991 – General MIDI – standardizes instrument definitions and controls, Roland General Sound expands instrument set further
incredibly easy to program, popular in sizecoding
late-90s ISA soundcards usually implements MPU-401 in UART mode, some (GUS/AWE32) able to emulate through wavetable engine

## Slide 32
development :: old toolchains
QuickBASIC?
  slow, and doesn’t have any decent sound capabilities without calling external code libraries
  besides, there are plenty of decent QBASIC demos (hey, DC5!)
Borland Pascal?
  you’re probably loved (or hated) it back in the days
  plenty of code examples and sound systems, all in one IDE
  poor code optimization, no 386 target support -> DB $66 HELL
  ending up making 90% of demo in assembly *shrug*
Turbo Assembler?
  while it is actually pretty decent choice…
  however coding in 32-bit protected mode is tricky (fortunately PMODE can save you from cracking your head)
  there are enough new and easier to use assemblers
… as time flies, we can choose better tools…

## Slide 33
development :: open watcom c\c++ ::
the flagship DOS development tool, popularized by DOOM (1993) and used by almost every major DOS title since
friendly 32-bit DOS environment – zero-based memory model (with 1st MB mapped 1:1 – no need to fiddle with segments), extended Int21 interfaces, comprehensive DPMI support, up to full 4GB
cross-platform – targets 16-bit and 32-bit DOS, Win16, Win32, Linux, OS/2, Netware, upcoming x86-64 support; can cross-build DOS apps under Windows/Linux
supported by lots of video/sound libraries
decent code optimization – not the best by today’s standards but still doesn’t struggle like SDCC on Z80 :)
language features support still near C++98/C99 levels (no C++11 sweetness, sorry)
active development ceased after 1997, has been open-sourced in 2002 then being maintained by enthusiasts

## Slide 34
development :: djgpp
a port of GCC toolchain for 32-bit DOS environment
updates frequently (last build in 2020 featuring GCC 10.2)
used by less software, Quake (1996) being the notable example
Easy cross-compiling on Windows/Linux host, good 3rd party IDE/code editor support
built-in GO32 DOS Extender- depends on DPMI host only
less memory-friendly than Open Watcom – non-zero based memory model – more stable but requires to change segments to access DOS memory/VGA framebuffer
great code optimization, latest C++17 features supported
scarcer library support (Allegro is pretty redundant for demos)
anyway a better (probably) than Watcom choice if you only want to blit frames and don’t go deep into hardware trickery (i.e. targeting Pentium/VGA/VESA), unsuitable for XT/286

## Slide 35
emulators :: virtual machines
don’t use them. Not even VMware. Not even Oracle VM VirtualBox.
since VMs are focused to run newer host systems, they don’t bother to emulate common features being used by DOS high-performance stuff (cycle-accurate VGA emulation, VBE, etc)
Bochs/QEMU is relatively decent, but still refrain from using them as first-class testing environment

## Slide 36
emulators :: dosbox
the easiest and most balanced way to test your DOS stuff :)
emulates DOS environment, can mount host folders as disks, floppy and CD images
vanilla DOSBox builds are games-oriented and feature-limited, doesn’t cycle-accurately emulate VGA well, had trouble with tricky stuff, seldom updates
…fortunately, as it’s open-source, better forks exist, i.e. DOSBox-X:
emulates everything from PC/XT to Pentium Pro/MMX, and even PC-98!
near perfect VGA emulation (still improving but runs 99% of demos great), great SB/GUS support, emulates SVGA (as S3 Trio64) and 3dfx Voodoo well
can boot and run Windows 3.x/95/98 (if you really wants it :)
works on Windows, Linux and macOS, and even able to run under real MS-DOS! :)

## Slide 37
emulators :: pcem
contrary to DOSBox and like other platforms emulators, emulates full PC environment
cycle-exact device emulation (the 8088+GCA configuration runs 8088 MPH almost perfectly)
emulates lots of devices (floppy and hard drives, CGA/EGA/VGA + several SVGA models, SB16/AWE32/GUS/Interwave, 3dfx Voodoo and much more)
easy to adjust configuration – from 8088/4.77MHz to Pentium MMX/II
uses real hardware ROMs (not HLE like DOSBox), you have to find them on the Internet and place in emulator ROM folder

## Slide 38
sizecoding
art of making audiovisual stuff in extremely tiny executables
(512 bytes or less )

## Slide 39
sizecoding :: why dos?