## Slide 1: MS-DOS demoscene 2021 - software rendering, sizecoding and modern approach to retro-demomaking
Artem Vasilev :: wbcbz7 @ Demodulation 2021

## Slide 2
why? what?
while most of other oldskool platforms live through surge of retrocomputer interest, PC is no an exception
did you ever wanted to make something for oldskool PC but were afraid of?
we’ll be focused on these topics:
PC/DOS scene origins and historic periods
hardware overview – from original IBM machines to late-90 midskool stuff
in-depth breakdown – x86, VGA and DOS/BIOS
“ms-dos scener 101” guide – development tools and environment
…and maybe even some livecoding (if we have enough free time :)

## Slide 3
why dos?
MS-DOS is, scene-wise, quite a curious platform…
being initially associated with “boring office typewriters”, in the 90s quickly made it’s own way on throwing competitors out of market with raw CPU power and open architecture
on the eve of millennium, while almost every PC software making it’s way on Windows, Linux or other OSes, DOS still stayed as appealing platform for multimedia audiovisual enthusiasts
  eventually moved onto Windows and DirectX/OpenGL, of course
close-to-metal experience, software rendering being the most natural way
very friendly environment for extremely tiny sized stuff
… it’s fun :)

## Slide 4
ms-dos demoscene :: distinctive periods
Original IBM PC machines
sizecoding
the birth (1990 – 1992)
286-386, EGA/VGA, Covox/SB
the golden age (1993 – 1996)
486, VGA, GUS
the transfiguration (1997 – 1999)
Pentium, SVGA, GUS/SB16

## Slide 5
ms-dos demoscene :: the birth
inspired by both cracktros and Amiga demoscene, started from simple EGA/VGA experiments with ripped samples and 4 channel mods.
Slideshow by Future Crew (1990) – first ever production with 4-channel MOD music
Megademo by The Space Pigs (1990) – the first big scene production, and it runs on EGA!
Scream Tracker 2 by Future Crew (1990-1992) – marking the start of PC trackers era

## Slide 6
ms-dos demoscene :: the birth:: 1991
…slowly drifting towards vector worlds ….
Vicky by The Space Pigs (1991)
Cronologia by Cascada (1991)
VectorDemo by Ultraforce (1991)

## Slide 7
ms-dos demoscene :: the birth :: 1992
eventually reaching Amiga level of complexity with rapid performance growth
Unreal by Future Crew (1992)
Amnesia by Renaissance (1992)
Assembly 1992 – the first major demoparty with PC compos

## Slide 8
ms-dos demoscene :: the birth :: 1993
... driving beyond four channel MODs with new trackers and hardware like GUS …
Second Reality by Future Crew (1993)
Crystal Dream II by Triton (1993)
Untitled by Dust (1993)

## Slide 9
ms-dos demoscene :: the golden age:: 1994
... quickly catching up with and beyond the new Amiga AGA capabilities …
Verses by Electromotive Force (1994)
No! by NoooN (1994)
Cyboman 2 by Complex (1994)

## Slide 10
ms-dos demoscene :: the golden age:: 1995
... expanding to high resolution and phong shaded duck.3ds land …
Caero by Electromotive Force (1995)
Stars: Wonders of the World by NoooN (1995)
Drift by Wild Light (1995)

## Slide 11
ms-dos demoscene :: the golden age:: 1996
Toasted by Cubic Team & $een (1996)
Inside by CNCD (1996)
Contrast by Oxygene (1996)
... sqeezing last bits from freedirs and lens flares …

## Slide 12
ms-dos demoscene :: the transfiguration :: 1997
Boost by Doomsday (1997)
Square by Pulse (1997)
Stash by The Black Lotus (1997)
... getting backed by Pentium and High Color …

## Slide 13
ms-dos demoscene :: the transfiguration :: 1998
te-2rb by TPOLM (1998)
Kkowboy by Blasphemy & Purple (1998)
State of Mind by Bomb (1998)
... moving towards design in lieu of code …

## Slide 14
ms-dos demoscene :: the transfiguration :: 1999
bakkslide 7 by Hellcore & Omnicolour (1999)
Discloned by Haujobb (1999)
moralhardcandy by Blasphemy (1999)
... and finally heading towards world of Windows …

## Slide 15
ms-dos demoscene :: current state
during 1999-2000, the PC scene almost entirely moved on Windows, exploring new 3D accelerated horizons, running towards more polygons and shaders….
but in recent 10 years with a strong retroscene movement pushing from above, the DOS scene starts to resurrect (or kinda?...)

## Slide 16
ms-dos demoscene :: current state
reserching platfoms known for so many years…
...and squeezing last bits from ancient PCs
8088 MPH by Hornet & CRTC & Desire (2015)
cöncept by Ümlaüt Design (2021)
Rave On by Satori & da Jormas (2018)

## Slide 17
ms-dos demoscene :: current state
… as well as packing visuals to as less bytes as you can
tube by 3SC (256b, 2001)
Memories by Desire
(256b, 2020)
Gyroid by Řrřola (128b, 2021)
Blake 32 by Marquee Design (32b, 2021)

## Slide 18
ms-dos demoscene :: my own experience
I also had quite a large scene career period associated with oldskool PC stuff (and still have :) so I’ve made a couple of demos back then…
uribin (2016) – Pentium/VESA 2nd @ multimatograf 2016
volatile (2016) – Pentium/HiColor 1st @ Chaos Constructions 2016
#vologda8df (2015) – 286/EGA (partyhack :) 2nd @ multimatograf 2015
blash (2015) – 486/Pentium/VGA 1st @ Demosplash 2015

## Slide 19
ms-dos demoscene :: my own experience
spirwd (2016) – 256b/FPU/VGA 2nd @ DiHalt 2016
pxor (2017) – 256b/8088/CGA! 7th @ Multimatograf 2017
mikrowave (2017) – HiColor
7th @ CC 2017
.. as well as tiny intros …

## Slide 20
ms-dos demoscene :: my own experience
oh. by the way, all of my Watcom stuff had been open sourced :) https://github.com/wbcbz7/watcom-stuff

## Slide 21
computers :: ibm pc and xt
originally IBM didn’t even intended to step on personal computer market
initial proposals were purchasing design from 3rd party like Atari, later IBM internal “Project Chess” working group developed a prototype
several CPUs were considered, notably TMS9900, MC68000 and i8086
in the end, i8088 (striped-down 8 bit bus 8086 variant) was choosen
in August 12, 1981 - IBM PC was introduced, with i8088 CPU, optional 8087 FPU, and 64 KB of RAM (expandable up to 256 KB), 5.25 inch single/double side FDDs and MDA or CGA display adapter
became a large success, sales exceeded IBM's expectations by as much as 800%, shipping 40,000 PCs a month at one point.
shipped with PC-DOS (customized IBM version of MS-DOS ), eventually made Microsoft the #1 software developer
gained instant and widespread software and hardware support
  open architecture and simple design extremely encouraged new developers
Later, in 1982, PC/XT entered the market
Added internal hard disk, entended expansion capability, pumped memory capacity up to 640 KB

## Slide 22
computers :: ibm pc/jr and tandy 1000
With the success of original PC, IBM tried to enter home and entertainment market with PCjr in 1984
enhanced sound and graphics capabilities
64 or 128 KB of unified (CPU and video controller shared) RAM
internal 5.25’ floppy drive and cartridge slot
ended up with numerous manufacturing and compatibility issues, becoming a failure
nevertheless, some games take advantage of PCjr capabilities
Tandy 1000 was produced by Tandy Corporation for Radio Shack shops, introduced in 1984
basically with same capabilities as PCjr, but fixed obvious flaws like allowing easier memory expansion and DOS compatibility
lower priced than most PC clones, received moderate success
later SX/LX models further fixed compatibility issues and added more features

## Slide 23
computers :: ibm pc/at
Released in 1984, marks the start of new PC era
new Intel 80286 CPU at 6 or 8 MHz
extended XT system bus to 16 bit (later known as ISA)
optionally bundled with new EGA graphics adapter
enhanced IRQ and DMA support (16 IRQs vs 8 in XT, added 3 16-bit DMA channels)
battery-backed real-time clock using MC146818 IC, with additional storage for date, time and system settings
expanded memory capacity up to 16 MB
1.2 MB 5.25 FDDs and 16-bit hard disk controller
still being functionally open design, actively cloned by many vendors
  modern PCs are also retain “AT compatibility” :)

## Slide 24
computers :: ibm ps/2
introduced in 1987
wide range of models – from 8086-based Model 20/25 to high-performance 486 and Pentium machines
software compatible with PC and AT, much like other PC clones
introduced 3.5 inch floppy drives, PS/2 keyboard and mouse interfaces, VGA display adapter and 72-pin SIMM memory modules
moved from 8/16-bit ISA bus to proprietary MCA bus, increasing performance but also locking out independent vendors
overall being more an attempt to control the entire PC market, ultimately failed
  IBM then turned into niche PC vendor, with notable ThinkPad laptop series

## Slide 25
computers :: meet the clones
After IBM PC success, other companies started to produce functional or full clones of original machine, often with expanded capabilities
IBM published schematics and detailed operation info in Technical Reference manuals, only BIOS remained copyrighted
  several vendors made clean room implementations, notably American Megatrends, Phoenix and Award Software
1982’s Columbia Data Products MPC 1600 is the first 100% IBM PC compatible clone
first i386 PC was produced by Compaq in 1986, year before IBM PS/2
by the end of 80s, PC clones became dominant in market, and IBM eventually lost control under PC ecosystem
  Intel and Microsoft became the leading force of PC evolution
MPC 1600
Compaq Deskpro 386

## Slide 26
computers :: meet the clones
..and since then, everyone could built their own PCs…

## Slide 27
hardware :: graphics cards
during active PC/MS-DOS era, graphics capabilities constantly got improving from business-grade text processing and four color on screen to high resolutions, sharp pixels and millions of colors

## Slide 28
graphics cards :: mda/hercules
MDA introduced with the first IBM PC in 1981
based on Motorola MC6845 CRTC
supports only monochrome 80x25 textmode with 9x14 charset -> 720x350 resolution at 50 Hz
included parallel port at 0x3BC
4kB of VRAM at 0xB0000
Later, Hercules released HCG with monochrome graphics mode, backwards compatible with MDA hardware/software
720x348 pixels, stored as 4-line interleaved bitmap due to 6845 limitations
64 kB of VRAM, with 2nd page at 0xB8000
cheap HGC cards were popular as both low-cost business and dual-head soultion for software debugging

## Slide 29
graphics cards :: cga
along with MDA, Color Graphics Adapter was also released
also based on Motorola MC6845 CRTC, but more entertainment and home use oriented
supports 40x25 and 80x25 text modes with 8x8 matrix -> 320/640x200 resolution @ 60 Hz
  80x25 mode uses entire DRAM bandwidth, “snow” artifacts apparduring screen updates while active area
supports 320x200 graphics mode with 4 colors and 640x200 mode with 2 colors
  + undocumented 160x100 16 colors mode (basically tweaked 80x25 textmode)
16kB of VRAM at 0xB8000, graphics mode layout is 2-line interlaced
drives both RGBI TTL (15 kHz) monitors and composite NTSC TVs/displays
  Due to simplified composite circuitry, hires modes create artifact colors, extending available colors to 1024 and more

## Slide 30
graphics cards :: cga :: magic trickery
by default, CGA support
two palettes in 320x200 mode + selectable 0th color + two intensity levels
  “monochrome” mode 5 actually activates 3rd palette on TTL monitor
selectable foreground color in 640x200 mode
while it sounds pale enough, complex visuals can be delivered with clever artist work

## Slide 31
graphics cards :: cga :: magic trickery
but as composite output lacks proper filtering, artifact colors are possible
  setting high-resoluition mode and using alternating patters allows to create artifact colors
  already often used in commercial games, like King’s Quest
  abused to the limit and beyond in 8088MPH, giving 1024 simultaneous colors on screen!
  check great article by VileR (if you still didn’t) for more details!
(screenshots from aforementioned write-up)

## Slide 32
graphics cards :: pcjr/tandy 1000
PCjr and Tandy 1000 both use similar graphics adapter, known as “Video Gate Array”
like MDA/CGA, also based on Motorola MC6845 CRTC
unified memory architecture – VRAM is shared with system RAM, MC6845 is responsible for DRAM refresh
all 16 colors can be redefined through the palette to any of 16 RBGI colors
three additional modes:
  160x200 16 colors, using 16 kB and 2-line interlaced, like CGA modes
  320x200 16 colors and 640x200 4 colors, 32 kB, 4-line interlaced (unavailable in 64kb models)
composite and TTL RGBI output

## Slide 33
graphics cards :: mda/cga/pcjr :: mc6845
Motorola MC6845 is one of most popular CRT controllers for personal and home computers
originally intended for character based displays
with additional circuity, graphics can be displayed
used in several popular 8-bit home computers
  BBC Micro and Amstrad CPC are notable examples
had only 14 bit address support – constrained to 16 kB of VRAM for graphics mode without remapping
maximum 7 bit vertical counter – limited to 128 rows without special tricks
  remapping character row address to high bits of memory address increases vertical graphics resolution
  that also explains “interlaced” framebuffer structure
manufactured by several vendors (Hitachi, UMC, Amstrad), implementations differ in edge cases
  known as CRTC types in CPC scene
  i.e. MC8645 is used in old CGA revisions and HD6845 in new

## Slide 34
graphics cards :: ega
introduced in 1984 along with IBM PC/AT line
based on custom chip design
four bitplane memory, 64 kB total in first model, later expanded up to 256 kB
dual-sync design, 16 colors out of 16/64 color palette
  8x8 character textmode and 320/640x200 16 colors from 16 on older CGA/RGBI monitors
  8x14 char textmode and 640x350 16 from 64 colors for EGA displays, plus 80x43 enhanced textmode with 8x8 character size
  monochrome 640x350 graphics/text for MDA/Hercules dispalys
complex read/write logic and data latches offloading CPU and permitting fast VRAM copies
programmable character set
VBLANK interrupt (rarely used, deprecated in VGA)
smooth scrolling, page flipping and split screen support
feature connector for interfacing with additional h/w
BIOS and memory layout-compatible with CGA
Original IBM EGA
ATi EGA Wonder

## Slide 35
graphics cards :: ega :: art
due to required compatibility with older CGA monitors, 200-line graphics modes are limited to 16 colors
that’s why most EGA games often look comparable with PCjr/Tandy in terms of colors
but thankfully to powerful EGA write logic and scroll capabilities, EGA games tend to feel more smoothly compared to PCjr titles
  Commander Keen being notable example, showcasing novel Carmack’s Adaptive Tile Refresh technique
bitplane graphics also favored fast flat-shaded 3D

## Slide 36
graphics cards :: ega :: art
as EGA monitors became widespreading, high resolution (640x350) games start to appear, making full advantage of enhanced RGB222 palette
most ex-USSR EGA software are HiRes, as imported machines were equpped with EGA monitors
strategic games also prefer EGA HiRes, like SimCity

## Slide 37
graphics cards :: ega :: demoscene
and moreover, there are plenty of demoscene releases for the EGA!
The MEGA-EGA Demo by S-Cubed
(1994)
1991 Donut by Desire (2013)
Gr8 by Future Crew (1990)

## Slide 38
graphics cards :: vga
introduced in 1987 in IBM PS/2 machines, later released as standalone (rare) ISA card
single-chip ASIC design, versatile and widely cloned :)
moved from digital to analog RGB, doubled scan rate to 31 kHz and vertical refresh to 70 Hz
RAMDAC allowing up to 256 color from 262144 3x6-bit palette
new graphics modes:
  8x16 character 40x25 and 80x25 text modes
  double-scanned CGA/EGA compatible 320x200/640x200modes with enhanced palette capabilities (16 sets of 16 colors from 256K palette)
  640x480 2/16 colors 60 Hz high resolution and 1:1 pixel aspect mode
  320x200 256 color linear (chain-4) graphics mode + various Mode-X unchained 256 modes
256 kB of VRAM, 4 bitplane arranged
register and memory layout compatible with EGA
became an instant hit, copied and enhanced countless tiles, supported by almost every OS since 90s, still supported by modern graphics cards
more in-depth VGA breakdown in “in depth” section
VGA integrated in IBM PS/2
Standalone IBM VGA card

## Slide 39
graphics cards :: vga :: super vga
original IBM VGA is pretty slow due to 8-bit CPU bus, and limited to low-res 256-color modes
several manufacturers copied VGA design, enhanced it with 16-bit host bus, FIFO buffers for optimizing VRAM access, faster and larger memory, higher resolution and color modes….
commonly known as “Super VGA” cards
  released from firms like Cirrus Logic, ATi, Tseng, Trident, Realtek…. varying in VGA compatibility but being totally incompatible between vendor SVGA modes
VESA standartized SVGA features with the release of BIOS Extensions (1989 and onward)
Cirrus Logic GD5420 (1992-1994) – solid low-cost Super VGA adapter, integrating VGA, RAMDAC and PLL in one IC
Tseng ET4000AX (1989) – best performance at the time, SVGA landmark for several years
Trident TVGA9000C (1992) – low-cost range adapter with abysmal planar/Mode-X performance

## Slide 40
graphics cards :: vga :: super vga
… later being extended by 2D acceleration features, moving from 16-bit ISA to 32-bit VESA Local Bus….
Cirrus Logic GD5429 (1992-1994) – common mid-range 2D accelerator and solid VGA chipset
S3 805 (1992) – mid-range SVGA 2D accelerator
Trident TGUI9400CXi (1993) – low-cost 2D accelerator (and still DOOM decelerator :)

## Slide 41
graphics cards :: vga :: super vga
Tseng ET6000 (1996) – fast VGA performance, not so good VGA compatibility
Matrox Millennium (1995) – best 2D acceleration and image quality, moderate VGA compatibility
S3 Trio64 (1994) – all-in-one chip, low-cost bestseller and perfect VGA compatibility
… transitionsing by mid-90s to PCI ...

## Slide 42
graphics cards :: vga :: super vga
NVIDIA RIVA 128 (1997-1998) – pioneering 3D, great and compatible VGA core
3dfx Voodoo (1996) – standalone 3D-only accelerator, marking the era of fast and smooth 3D on the PC
S3 ViRGE (1995) – miserable 3D, nice 2D and perfect VGA compatibility
… approaching 3D acceleration and moving even further...

## Slide 43: hardware :: sound devices
originally PC has never been a multimedia machine
but as PC install base quickly went beyond corporate and office, growing CPU power became appealing for entertainment uses

## Slide 44
sound devices :: pc speaker
the most distinctive and ubiquitous PC sound device :)
supported all the way from first IBM PC to recent machines, and literally by every PC OS
originally used for system diagnostics and simple beeps, later being “enhanced” to digitized PWM samples and multichannel music
from hardware side, it’s basically:
1-bit output from PIT Channel 2…
ANDed with port 0x61 bit 0 (+ PIT gate @ bit 1)
but let alone PWM, the square wavy nature of sounds and one channel is more than enough!
(check System Beeps musicdisk and 8088MPH, also Monotone tracker
PC Speaker on original IBM PC 5150 (image by PixelatedArcade)

## Slide 45
sound devices :: pc speaker :: realsound
with a bit of trickery (Ch2 in Mode 0 + IRQ0 at sample rate), an aprx. 5-6 bit PWM sample playback is possible
cons: IRQ0 eats CPU time, audible squeak at sample rate, audio quality degrades with sample rate increase (20 KHz is realistic limit, giving 50 levels – almost 6 bits)
widely supported by software, incl. majority of DOS trackers and module players (ST2/FT2/IT), as well as by early DOS demos and games (known as RealSound)

## Slide 46
sound devices :: pcjr/tandy 1000
PCjr and Tandy 1000 machine were equipped with SN76489 programmable sound generator IC
three square wave channels
one noise channel, with 3 predefined frequencies + chained from secon channel
16 volume levels
used also in BBC Micro, TI-99/4A and SEGA Master System
PCjr and Tandy 1000 games take advantage of enhanced sound capabilities, but since demoscene on those machines is still a rare thing, not much

## Slide 47
sound devices :: covox
a totally simple and cheap DIY 8-bit DAC for parallel port
originally introduced in 1987 as Covox Speech Thing, become widespread as DIY device
provides full 8-bit sample resolution, (depends on DAC accuracy but still generally better than PC Speaker)
enhanced versions (stereo on one/two LPT ports, DAC ICs, filters and amplifiers, ADC capability, ISA cards, etc)
adapted and further enhanced for almost every 8/16-bit platform (Amstrad CPC, ZX Spectrum, MSX, etc)
enhanced variant known as Disney Sound Source added 16-byte FIFO and built-in loudspeaker, partially compatible with original Covox but has own diffirences

## Slide 48
sound devices :: covox :: build it yourself!

## Slide 49
sound devices :: covox :: example and notes
speaking of trackers/players/demos - almost every software supporting PC Speaker in RealSound mode supports Covox also. handles up to 44/48 KHz pretty well
stereo modes are different story, though – at least 3 incompatible Stereo-on-one-LPT protocols + two-port variant.
Covox Inc. also supplied digital sound drivers for Windows 3.x, although not much stable

## Slide 50
sound devices :: opl2/3
Yamaha YM3812 OPL2 FM synthesizer, introduced to PC with Adlib Music Synthesizer card in 1987
9 two-operator FM channels + percussion mode
4 waveforms, mono out
no PCM output capability, although it’s possible to get logarithmic 6bit DAC via FM operator tricks
easy to program, requires long delays between register writes (doesn’t matter much for XT, but becomes cumbersome on 286 and faster)
supported by most ISA soundcards (popularized by original Sound Blaster, two OPL2 in SB Pro)
supported by majority of DOS games, frequently used in BBS intros and cracktros

## Slide 51
sound devices :: opl2/3
later YMF282 (used in SB Pro 2/16 and Adlib Gold) is backwards software compatible with OPL2
18 2-OP or 6 2-OP + 6 4-OP FM channels, stereo capability, 4 new waveforms
reduced access delays
many later ISA sound chips implement custom OPL3 compatible cores (Creative CQM, ESFM, etc.), with varying sound faithfulness to the original OPL3
most OPL trackers supports OPL2 feature level (HSC, RAD, AMusic, Scream Tracker 3), others like Adlib Tracker support OPL3 features
Adlib Tracker II

## Slide 52
sound devices :: sound blaster
released in 1989, introduced DMA PCM to PC market
bundles OPL2 for Adlib Compatibility + two SAA1099, “DSP” chip (relabeled Intel 8051 MCU) handles PCM playback/recording + ADPCM playback + MIDI
originally supported max. 23 kHz 8 bit mono, later SB 2.0 added auto-init DMA capability for buffered playback + hi-speed mode for 44 kHz audio
relatively easy to program, supports DMA/IRQ for CPU offloading
quickly become a market success, supported by many DOS games, demos are quite different story though
Original SB 1.0 (CT1320)
SB 2.0 (CT1350)

## Slide 53
sound devices :: sound blaster pro/16
SB Pro finally added stereo PCM + OPL playback
max 22 kHz 8 bit stereo or 44 kHz 8 bit mono
de-facto standard across ISA soundcards, often enhanced with own extensions (ESS cards)
later SB Pro 2.0 uses single OPL3 instead of two OPL2
SB 16 introduced 16-bit CD-quality PCM + MPU-401 compatible MIDI interface
44 kHz 16 bit stereo, backwards compatible with SB 2.0 but not SB Pro’s stereo mode
games rarely take advantage of 16-bit capabilities, but many trackers/demos/players support SB16 for better sound quality (still can’t beat the GUS :)
SB 16 CT2940
SB Pro 2.0 CT1600

## Slide 54
sound devices :: gravis ultrasound
the DOS demoscene golden standard :)
released in 1992, used GF1 chip + onboard RAM for wavetable synthesis and sample playback
32 wavetable channels with linear interpolation, volume, pitch and panning control, up to 44 kHz 16 bit hardware mixing (full 32ch is 19 kHz though)
up to 1 MB of onboard RAM, 8/16bit samples
No Adlib/SB compatibility, PCM streaming has to be done by free wavetable channel + DMA
very easy to program – ideal for tracked music
almost all post-1993 demos support GUS (often as sole sound device), as well as trackers and players
GUS Ace
Classic GUS with 1 MB RAM

## Slide 55
sound devices :: gravis ultrasound :: max/pnp
GUS MAX bundled CS4231A codec for streamed PCM capability and better SB emulation
in 1995, AMD develops Interwave IC, used in GUS PnP and several 3rd party cards
full 32 channels at 44 kHz + MPU-401 MIDI
up to 16 MB of sample RAM (upgradeable with 30-pin SIMMs) + 1 MB ROM
backwards compatible with GF1
some demos/players support Interwave natively, other will work fine in classic GUS mode
GUS PnP with 2.5 MB
GUS MAX

## Slide 56
sound devices :: sound blaster awe32/64
basically SB16 + EMU8000 wavetable synthesizer
32 wavetable channels with 4-point interpolation, volume, pitch and panning control, up to 44 kHz 16 bit mixing + resonant filters + effect processing
16-bit only always-looped samples, up to 28 MB RAM + 1 MB ROM
Creative originally didn’t disclosed register details, several people reverse engineered EMU8000 internals then finally official hardware reference has been released
needs complex init compared with GUS, wavetable limitations (max 176 kHz pitch, 16 bit samples, etc.)
not as common as GUS, supported by some trackers (e.g. IT2) and demos
SB AWE64 Value (CT4380)
SB AWE32 (CT3990)

## Slide 57
sound devices :: midi
originally used for music equipment control
1984 – Roland MPU-401 – universal MIDI interface, supports many platforms, incl. PC, support UART and intelligent accelerated mode
1987 – Roland MT32/LAPC-1 – reference music synth for early DOS games
1991 – General MIDI – standardizes instrument definitions and controls, Roland General Sound expands instrument set further
incredibly easy to program, popular in sizecoding
late-90s ISA soundcards usually implements MPU-401 in UART mode, some (GUS/AWE32) able to emulate through wavetable engine
Roland LAPC-1

## Slide 58
storage :: cassette interface
yes, you heard it right – original IBM PC did included tape interface!
supported by BASIC and system BIOS, not that much useful
…you can even boot MS-DOS from vinyl :)
… or load apps via tape interface using 5150CAXX
PCjr also had similar cassette interface (with different connector), but practically never used
Several soviet IBM PC clones (i.e. Poisk-1) support cassette interface and ported some software on the tape

## Slide 59
storage :: floppy disk drive
available in original IBM PC, upgraded in AT and PS/2
initially 5.25” single/double sided 40 track drives (180/360 kB)
Later IBM PC/AT introduced 1.2 MB 80-track drive
IBM PS/2 switched to 3.5 inch 720 kB/1.44 MB disks
  720 kB disks were uncommon, supported with 3rd party drivers like 800.com or PU_1700 (also enabling non-standard formats up to 1.76 MB)
based on NEC uPD765 / Intel i8272 floppy disk controller and modified Shugart floply interface
  max. two drives per ribbon, both drives are configured as drive B (cable is twisted between drives accordingly), Disk Changed signal in place of Ready
supports DMA read/write, offloading CPU
FAT12 is used as primary file system
early games often distributed as PC booter, allowing to boot directly from floppy, eliminating the need for booting MS-DOS

## Slide 60
storage :: hard disk drive :: st-412/506
Originally added in IBM PC/XT, uses Seagate ST-412/506 hard disk and their interface
provides own BIOS extending Int13 services
most 8-bit ST-412/506 controllers are incompatible between each other, requiring disk low level formatting
IBM PC/AT used new 16-bit ST-402/506 controller by Western Digital
hard drive support included in system BIOS
initially only several predefined types of hard drive supported, later clone BIOSes (AMI, Phoenix, Award) extended by supporting user defined types and even autodetecting
generally, 16-bit ST-412/506 controllers are compatible
  Later disk controller electronics moved on hard drive, providing basis for ATA/IDE interface

## Slide 61
storage :: hard disk drive :: ata/ide
Introduced in late 80s by Western Digital, based on standard PC/AT hard disk controller
Universal 40-pin interface, basically 16-bit ISA extended with address decoding schematic
Replaced ST-412/506 in early 90s, providing low cost and easily expandable storage solution, eventually made its way as industrial standard and adopted by other platforms (Amiga, Atari ST/Falcon, etc.)
Supported CHS addressing, LBA added in later versions
Initially HDD-only, later adopted CD-ROM and other media types via ATAPI protocol
In mid-90s, Western Digital and Phoenix Technologies further updated the interface (Enhanced IDE), adding DMA modes, increasing capacity and standardizing geometry translation
Later UltraATA specifications added CRC control and speeded up interface to 33-133 MB/sec
Replaced during 2000s by Serial ATA, which still provides compatibility layer with IDE interface (both in software and via SATA-IDE converters)

## Slide 62
storage :: today
Floppy interfaces are easy to use
USB-FDD work fine with 1.44 MB floppies, some can read and write 720k disks
3.5 inch drives are dirt cheap, modern pc (from 2010) don’t support internal floppy drives, though
5.25 are harder to find, otherwise same considerations as for 3.5 inch apply altetnatively, you can use FDD emulators like Gotek (preferably flashed with custom firmware like HxC or FlashFloppy)

## Slide 63
storage :: today
Interfacing with hard disks is also relatively easy
For PC/XT, XT-IDE controller provides full IDE interface, supporting up to 2 or 4 drives
For AT and better class machines, all you need is cheap I/O multi controller (preferably buffered)
Late 486 and newer machines are equipped with built-in IDE controllers
Alternatively, discrete PCI-SATA or ISA/PCI-SCSI controllers can be used with corresponding drives
Instead of noisy old HDD, you can opt for SD-IDE, CF-IDE converter or even IDE-SATA with SSD (like I did on my P3 class machine :)
ATAPI emulators available, emulating CD/DVD drives from SD or USB flash
  unfortunately they are either in development or quite costly
  USB-DVD + bunch of CD-RWs + real IDE CD/DVD drive is still way cheaper
USB flash drives are exotic option under DOS (drivers exist but not guaranteed to work in every case), but if you have PC with USB port and Windows 9x installed, then why not?

## Slide 64
storage :: today :: limitations
unfortunately, many systems imply HDD capacity limitations
  (NOTE: this applies to IDE drives and system BIOS only!)
earlier AT BIOSes (including clones like AMI up to 1993) can’t work with drives more than 528 MB due to CHS addressing overlapping limits
with EIDE drives and geometry translation, Int13 limit is raised to 8 GB
  you can still boot from larger drive, make sure boot partition is located at start of drive space. Windows 9x doesn’t care about these limitations, but you may need to use disk overlays like EZ-Drive or Ontrack Disk Manager for accessing entire drive under DOS
Award BIOS versions before 1999-2000 hang while detecting hard drives over 32/64 GB, unless BIOS is patched or updated
  that’s really breaking issue, you have to use 32GB limit jumper or patch/update your BIOS
almost all pre-2002 machines imply 127 GB limit, though these disks can still work with other OSes like Windows
discrete controllers with expansion ROMs has own separate limitations (XT-IDE doesn’t have capacity limits, for example, and can work with any HDD size)

## Slide 65
in depth :: x86
about cpu itself

## Slide 66
in depth :: x86 :: registers
  7 general purpose registers
  mostly orthogonal since i386,
  EAX

## Slide 67
in depth :: x86 :: opcodes

## Slide 68
in depth :: x86 :: modes

## Slide 69
x86 :: memory model :: real mode
In real mode, memory pointer is constructed from two components: segment and memory offset
segment value defines memory start address in units of 16 byte (paragraphs)
then, 16-bit or 32-bit offset is added to resulted segment value to form memory linear adress
segments can overlap: i.e. 0x0000:0482 and 0x0040:0082 point to same memory address 0x000482
i286 and higher calculate addresses in full 24/32bit: address overflow is possible with segments > 0xF000, allowing access to 64 Kb (minus 16 bytes) above 1 MB
  called High Memory Arena (HMA) in DOS world
  on 8086/8088, addresses beyond 1 MB are wrapped to start of memory: some older software depend on this behavior, and IBM implemented A20 line gate to emulate such wraparound

## Slide 70
x86 :: memory model :: real mode
In real mode, memory pointer is constructed from two components: segment and memory offset
segment value defines memory start address in units of 16 byte (paragraphs)
then, 16-bit or 32-bit offset is added to resulted segment value to form memory linear adress
segments can overlap: i.e. 0x0000:0482 and 0x0040:0082 point to same memory address 0x000482
i286 and higher calculate addresses in full 24/32bit: address overflow is possible with segments > 0xF000, allowing access to 64 Kb (minus 16 bytes) above 1 MB
  called High Memory Arena (HMA) in DOS world
  on 8086/8088, addresses beyond 1 MB are wrapped to start of memory: some older software depend on this behavior, and IBM implemented A20 line gate to emulate such wraparound

## Slide 71
x86 :: memory model :: protected mode
In protected mode, segment registers do not contain offset, instead, descriptor selector is used
defined as 13-bit selector field, Global/Local Descriptor Table select bit and requested privilege field (2 least bits)
each GDT/LDT entry contain of 8 bytes descriptor with defined stasrt offset, limit, descriptor type and access rights (whether is executable, read, write, etc., privilege level, etc)
CPU checks access rights and descriptor validity while segment register usage, raising General Protection Fault in case of failure

## Slide 72
x86 :: memory model :: protected mode
while segmentation still was crucial for 286 because of 16 bit offsets, 386 and 32-bit modes do not generally need it
“flat” mode involves setting CS to code segment and DS/ES/SS with data segment, noth with base 0 and limit of 4 GB, effectively bypassing segmentation and treting every logical address as linear
i386 also introduced memory paging unit

## Slide 73
x86 :: memory model :: flat real mode
apparently, 80386 and newer CPUs use same segment descriptor pipeline for both real and protected mode, differing only in address calculation
each segment register has associated descriptor cache
it’s possible to enter protected mode, set all data segments to 4 GB limit and switch back to real mode, allowing to access data over first MB while retaining compatibility with DOS/BIOS services and interrupts
requires raw or XMS environment, most PM supervisors (like EMM386/Windows) don’t allow such tricks and either reset segment limits to 64 KB upon return to RM or terminate the application
used in several early (pre-1995) demos and even some commercial games (Ultima 7/8)
expanding CS limit over 64 KB or switching to 32 bit code segment is practically useless (RM IRQs corrupt high 16 bits of EIP, and DOS/BIOS code won’t work in 32-bit real mode)
  nevertheless, there is at least one demo (Project Angel by Impact Studios, 1994) using 32-bit flat real mode
With the availability of DOS extenders, 32-bit protected mode is more attractive and easier to use than flat real mdoe

## Slide 74
in depth :: interrupts
Irqs and software interrupts

## Slide 75
in depth :: isa dma

## Slide 76
in depth :: timing
PCs are usually employ several timing methods:
Programmable Interval Timer Channel 0 at IRQ0
  running at 18.2 Hz by default, used by BIOS for disk timeouts and time counting
  the primary and precise enough universal timing source
  often being used by TSRs and sound systems, needs precautions for timer sharing
RTC timer at IRQ8 (AT and higher)
  counts at rates from 8 up to 8192 Hz, with power-of-two frequency step
  unused by BIOS routines by default, easy to interface (example in rtc_test folder)
Time Stamp Counter (Pentium and higher)
  Incremented each CPU clock, available by RDTSC instruction in EDX:EAX
  needs calibrating to other timing source (i.e. IRQ0) before use, provides extremely precise timing, very useful in profiling
VGA Vertical Retrace bit in Input Status Register (port 0x3DA bit 3)
  unfortunately VBLANK IRQ is deprecated on VGA and unavailable, and port polling can result in retraces being mussed, causing slowdowns

## Slide 77
in depth :: vga
your working horse for DOS journey :)

## Slide 78
in depth :: vga :: access
Memory Address | Description
0xA0000 – 0xAFFFF | EGA/VGAs framebuffer
0xB0000 – 0xB7FFF | Monochrome framebuffer
0xB8000 – 0xBFFFF | Color text and CGA famebuffer
I/O Port Address | Description
0x3C2/0x3CC | Miscellanous Output Register
0x3D4-3D5/0x3B4-3B5 | CRT Controller Index/Data
0x3C4-3C5 | Sequencer Index/Data
0x3DA | Input Status Register
0x3CE-3CF | Graphics Controller Index/Data
0x3C0/0x3C1 | Attribute Controller Index/Data (combined)
0x3C6-3C9 | RAMDAC Registers

## Slide 79
in depth :: vga
CRT Controller
generates all the necessary display timings, provides memory address for display refresh
Sequencer
generates basic display timings (dot and character clock), arbiters VRAM accesses between CPU and CRTC, protects bitplanes for being changed
Graphics Controller
interfaces between display memory and both attribute controller and CPU, converts and translates VRAM data, performs complex CPU write/read logic for speeding up access
Attribute Controller
formats input graphics and text data to pixel stream, handles blinking, underline and cursor logic
RAMDAC
converts digital pixel stream throung color lookup table to RGB triplets, then converting RGB digital data to analog
Many SVGA cards add additional functions, e.g. 2D/3D acceleration, fast FIFO interface to VRAM, etc.

## Slide 80
in depth :: vga :: graphics controller
Setting individual pixels with bitplane structure is slow
Read from all 4 bitplanes, modify, write back
VGA includes special circuity for speeding up
common graphics tasks
Latches work as 4 8-bit buffers between VRAM, and graphics controller logic, loaded with VRAM data at CPU read address
Read modes include either reading one selected bitplane, or comparing latches data against reference color, allowing pattern searching and fast flood fills

## Slide 81
in depth :: vga :: write modes
Write Mode 0:
CPU data rotation
Individual plane Set/Reset control for plane masking
ALU operations: move\AND\OR\XOR
Masking individual pixels by bit mask
ideal for pattern fill
Write Mode 2:
CPU data replicating “color” bitwise for all pixels in 8x1 block
ALU operations: move\AND\OR\XOR
Masking individual pixels by bit mask
suitable for plotting individual 16c pixels or Mode-X line drawing

## Slide 82
in depth :: vga :: write modes
Write Mode 1:
direct latch->VRAM copy
as latches are loaded for each byte read from memory, this can be used for fast VRAM->VRAM blits
Write Mode 3:
CPU data rotation and masking with bit mask, used as bitwise “selection” between latch data and constant color
suitable for pattern or line drawing in 16 color modes

## Slide 83
in depth :: vga :: 16 color modes
known from EGA days and 640x480 HiRes modes, being greatly enhanced in VGA:
16 sets of 16 colors, out of total 262144 colors
split screen and smooth scrolling
up to 8 video pages
200-lines mode double scanning improving graphics quality
bitplane structure, ideally suited for flat-shaded 3D and translucency effects
lots of VGA demos and games take advantages of 16-color modes for fast and smooth action

## Slide 84
in depth :: vga :: 16 color modes

## Slide 85
in depth :: vga :: 256 color mode
the most innovative addition to VGA, giving vivid colors and outperforming competing platforms
linear memory layout (one byte – one pixel), ideal for graphics applications, faster than planar approach and giving green light to fast paced 3D action FPS
wide palette range – 64 RGB levels, total 262144 colors palette
cons: chained on top of EGA planar architecture, wasting ¾ of VRAM and permitting one page only :(

## Slide 86
in depth :: vga :: 256 color mode

## Slide 87
vga :: 256 color mode :: mode-x
discovered by several people, popularized by Michael Abrash, the way of disabling plane chaining results in faster
entire VRAM is useable, allowing 4 pages in 320x200 mode, smooth scrolling/panning, double\triple buffering and high resolutions up to 360x480
Write Mode 1 (VRAM copy) can be used for fast sprite and image objects blitting
somewhat ankward memory layout, still pretty fast for column filling
  early 3D shooters like Wolfenstein 3D (1992) and DOOM (1993) render walls as textured columns of constant depth, which is equally fast in both Chain-4 Mode 0x13 and Mode-X, while the latter having advantage of multiple page buffering

## Slide 88
vga :: 256 color mode :: mode-x

## Slide 89
in depth :: vga :: text mode
the good ol’ textmode got also heavily upgraded in EGA and VGA:
up to 8 user-defined character fonts, 1 or 2 on screen
blink, underline and hardware cursor effects
smooth text scrolling and panning
high character resolution – 9x16 font, 1-32 lines
enhanced capabilities were hugely praised by ASCII/ANSI scene

## Slide 90
in depth :: vga :: text mode

## Slide 91
in depth :: vga :: color pipeline

## Slide 92
in depth :: vga :: color pipeline :: colors
attribute controller palette colors
with Color Page registers, either 4 sets out of 64 colors or 16 sets out of 16 can be selected with one register write
RAMDAC palette colors
total 3x256 colors = 768 bytes, Red first then Green and Blue; palette index is autoincremented for batch color updates

## Slide 93
in depth :: vga :: split screen
ability to scroll playfield independently of bottom bar
static graphics is placed at offset 0
CRTC Line Compare register sets to number of split line
when split line is reached, display address counter resets to 0

## Slide 94
in depth :: vga :: scrolling
smooth scrolling\panning as combination of CRTC and attribute controller functions

## Slide 95
in depth :: vga :: scrolling
smooth scrolling\panning as combination of CRTC and attribute controller functions

## Slide 96
in depth :: vga :: scrolling :: precautions
unfortunately, scroll settings are distributed among 4 registers:
Horizontal Pixel Panning (attribute controller index 0x13, pixel-precision H scroll)
Preset Row Scan (CRTC index 0x8, pixel-precision textmode V scroll)
Start Address (CRTC index 0xC/0xD) – start position in pixels or characters
moreover, CRTC and ATC registers are latched once and cannot be changed mid-frame
CRTC registers are latched at leading edge of VSYNC pulse (port 0x3DA bit 3 0->1 transition)
Horizontal Pixel Panning latched at start of display enable (port 0x3DA bit 0 1->0 transition)
and to make everything complicated further, some SVGAs (ATi, Matrox) latch scroll registers at different positions than most of VGA cards (check marvellous Gona’s compatibility chart)
solution: update CRTC registers during active display, update ATC registers on VSYNC (port 0x3DA bit 3 0->1 transition)
side advantage: pseudo-triple buffering

## Slide 97
in depth :: vga :: black magic
even if changing start address midscreen is not possible, there are still lots of usable tricks
polling for display enable (port 0x3DA bit 0) for tracking HSYNC and changing palette mid-line
  COPPER BARS! AMIIIIGAAAAAAA!
Setting Offset register (CRTC index 0x13) to 0 – displays same line on every scanline
  kefrens bars, Y-zooms and even crude X-wobbles
resetting split screen position multiple times per frame, changing modes mid-frame
oddball graphics modes: 16 color linear, 256 color semi-planar, CGA chain-4, etc.
simulating true color modes on standard VGA with color interlacing
…and much much more :)
SVGATRIX by Type One/TFL-TDV serves well as reference

## Slide 98
in depth :: vga :: black magic
Kukoo 2 by TFL-TDV (1994) – breaking every rule in the book

## Slide 99
in depth :: vga :: aspect ratio and refresh rate
common VGA modes (except for 640x480) are 16:10 and runs at 70hz vertical
while being displayed on 4:3 monitor, graphics is being distorted
70 Hz refresh considered as advantage during CRT era, but nowadays causes troubles with modern frame grabbers and displays
with CRTC tweaking, 320x200 letterboxed 60hz modes can be achieved

## Slide 100
in depth :: vga :: bios
VGA adapters typically contain ROM with BIOS firmware, providing video services via Int 0x10
mode set with AH= 0
pixel set/get (slow, but often used in sizecoding)
palette loading functions (AH = 0x10)
text output (notable functions are TTY output (AH=0E) and string write (AH=0x13))
font manipulations (AH = 0x11): charset uploading, font pointer retireving
graphics page, text scrolling and cursor control
…and some more
besides, some aspects of VGA programming are easier to interact via BIOS than direct programming, and vice versa

## Slide 101
in depth :: vesa bios extendions
by the early 90s, VGA limitations became obvious, and Super VGA adapters were not quite compatible from software side
i.e. 640x480 256 colors uses 300 kB of VRAM, requiring bank switching or linear frame buffer
  every vendor used its own hardware method to select banks, and bank size/granularity differ from each other
  moreover, even SVGA mode numbers were different between vendors!
High/True Color modes (16/24/32 bits per pixel) are starting to gain attention, first appearing on professional accelerators, then making its way on mass market
while it wasn’t such an issue for Windows applications or popular software packages like AutoCAD, because they implemented own driver model, independent from VGA BIOS API, DOS applications have to reimplement support for each VGA chip
as result, in 1989 Video Electronics Standard Association (VESA) developed a unified API for accessing SVGA features from bios and DOS applications, called VESA BIOS Extenstions (VBE)

## Slide 102
in depth :: vesa bios extendions
key features:
extending VGA BIOS Int10 calls with new API (AH = 0x4F)
standard interface for graphics adapter information retrieving and display mode enumeration
mode numbers are extended to 15 bit (+ VRAM clear request bit), with common modes being pre-assigned
unified interface for bank switching, either via Int10 or direct procedure far call
support for smooth scrolling, virtual screens and page flipping
starting from VBE 2.0 (1994), Linear Frame Buffer support added, eliminating the need of bank switching for 32-bit protected mode applications
  also, protected mode VBE interface was inplemented, although not much used in software
VBE 3.0 (1998) added refresh rate control and stereoscopic display support
unfortunately, not every graphics chip vendor did implemented VBE correctly, causing incompatibility issues (missing LFB support, no lowres modes, scrolling issues, etc.)
SciTech Display Doctor (aka UniVBE) is alternative VBE driver for numerous SVGA cards, implementing full VBE specifications with additional features

## Slide 103
in depth :: vesa bios extendions :: in demos
lots of late 90s demos use either one of these mode
640x480 256 colors, sometimes 16/32 bpp also
low resolution Hi/True Color modes, like 320x240 16/32 bpp
exotic 15 and 24 bpp modes are not uncommon
same with oddball resolutions like 400x300 and 512x384 (half of 800x600 and 1024x768, respectively)
some productions don’t respect screen pitch(aka logical width)
resulting in squashed or skewed picture on some SVGAs

## Slide 104
in depth :: dos

## Slide 105
development :: getting started

## Slide 106
development :: old toolchains
QuickBASIC?
  slow, and doesn’t have any decent sound capabilities without calling external code libraries
  besides, there are plenty of decent QBASIC demos (hey, DC5!)
Borland Pascal?
  you’re probably loved (or hated) it back in the days
  plenty of code examples and sound systems, all in one IDE
  poor code optimization, no 386 target support -> DB $66 HELL
  ending up making 90% of demo in assembly *shrug*
Turbo Assembler?
  while it is actually pretty decent choice…
  however coding in 32-bit protected mode is tricky (fortunately PMODE can save you from cracking your head)
  there are enough new and easier to use assemblers
… as time flies, we can choose better tools…

## Slide 107
development :: open watcom c\c++ ::
the flagship DOS development tool, popularized by DOOM (1993) and used by almost every major DOS title since
friendly 32-bit DOS environment – zero-based memory model (with 1st MB mapped 1:1 – no need to fiddle with segments), extended Int21 interfaces, comprehensive DPMI support, up to full 4GB
cross-platform – targets 16-bit and 32-bit DOS, Win16, Win32, Linux, OS/2, Netware, upcoming x86-64 support; can cross-build DOS apps under Windows/Linux
supported by lots of video/sound libraries
decent code optimization – not the best by today’s standards but still doesn’t struggle like SDCC on Z80 :)
language features support still near C++98/C99 levels (no C++11 sweetness, sorry)
active development ceased after 1997, has been open-sourced in 2002 then being maintained by enthusiasts

## Slide 108
development :: djgpp
a port of GCC toolchain for 32-bit DOS environment
updates frequently (last build in 2020 featuring GCC 10.2)
used by less software, Quake (1996) being the notable example
Easy cross-compiling on Windows/Linux host, good 3rd party IDE/code editor support
built-in GO32 DOS Extender- depends on DPMI host only
less memory-friendly than Open Watcom – non-zero based memory model – more stable but requires to change segments to access DOS memory/VGA framebuffer
great code optimization, latest C++17 features supported
scarcer library support (Allegro is pretty redundant for demos)
anyway a better (probably) than Watcom choice if you only want to blit frames and don’t go deep into hardware trickery (i.e. targeting Pentium/VGA/VESA), unsuitable for XT/286

## Slide 109
development :: assemblers
Flat Assembler (FASM)
relaxed syntax compared to TASM, easy to use
targets 16/32/64 bit code, supports all instructions from 8086 to AVX2
outputs .COM/binaries, MZ/PE EXE, ELF and COFF object files
open source, active community
cross platform, runs under DOS, Windows and Linux
well suited for sizecoding
Netwide Assembler (NASM)
feature-wise comparable to FASM, has more complex and versatile macro facility
in addition to FASM output formats, supports a.out, OMF, Mach-O and more
also open source, runs on Windows, Linux, macOS, DOS and even KolibriOS
overall a slightly better choice than FASM

## Slide 110
development :: ide
depends on what you want to do
for simple projects (like tiny intros), text editor like Notepad++ or Sublime Text + console is enough
complex stuff often requires some kind of building system + comprehensive IDE
Visual Studio Code is popular and versatile IDE choice
  doesn’t like Watcom C++ stuff much, needs some tweaks
    Since Watcom’s C++ dialect closely resembles Microsoft compilers, “msvc-x86” works pretty well
    https://github.com/intbeam/watcom-vscode suits well as template
  DJGPP and pure x86 asm is almost out of box
makefiles are fine, CMake is also a decent choice for crossplatform projects
  supports targeting both Watcom C++ and DJGPP

## Slide 111
development :: debugging
for 16-bit apps, Turbo Debugger suits pretty well, if you really love to debug on real thing
Watcom C++ package comes with own versatile debugger (wd.exe)
comes with both DOS and Windows (console and GUI wdw.exe) versions
supports remote debug via serial link, TCP/IP, named pipes or Win 9x DOS session
  serial null modem is most stable and useable option
debugs both 16-bit and 32-bit DOS executables
for DJGPP, gdb is the number one choice
also supports serial link debugging
of course, you have to compile your application with debug information to see anything other than pure asm :)
DOSBox and Bochs comes with their own built-in debuggers
best suitable for debugging system-related code

## Slide 112
development :: graphics/music
the choice of graphics tool depending on what type of graphics do you prefer
pixelart: aseprtie, usenti, GrafX2, Multipaint, etc.
illustrative gfx: better you know :)
batch processing/conversion: ImageMagick, Image Alchemy
regarding the music, it mostly depends on your preferred sound device:
PC Speaker: MONOTONE, PCSPE VSTi plugin, Vortex Tracker II
OPL2/3: Adlib Tracker II, several native DOS OPL trackers OpenMPT, Scream Tracker 3
modules: OpenMPT, MilkyTracker, FT2/PT2.3D Clone, native DOS trackers (ST3/FT2/IT2)
streaming ADPCM/MP2/MP3: any DAW you like :)

## Slide 113
development :: sound system
as already stated, this heavily depends on what you want to play
PC Speaker: write your own routine, it’s not that hard
  tip: many PC games supporting PC speaker play raw periods dump
OPL2/3: depends on target platform
  most DOS OPL trackers come with player routine, although it’s almost always 16-bit real mode
  for 32-bit, you can abuse game MIDI libraries like AIL or HMI, but that would be totally overkill
  as alternative, convert module to OPL register dump and play with custom routine, much like PC Speaker case
streaming music (ADPCM/MP2/MP3):
  unfortunately, didn’t was a thing back in the days, and comparing to Amiga/Atari Falcon scene, no suitable streaming music players are available
  theoretically MIDAS 1.1.2 can play ADPCM samples, albeit I didn’t tested that yet
  alternative 1: grab amp/mpg123/State of Mind (1998) demo sources, add SB output routine, done
  alternative 2: cut your music into long samples, put into XM/IT, play with module player (see below)
  extra tip for DJGPP users: use Allegro for playing in background (branch approves)

## Slide 114
development :: sound system :: mods
tracked modules: the sweet spot of DOS scene :)
16 bit – forget about XM/IT
MIDAS 0.40a is the best you can have, plays MOD/S3M, links with ASM/C/Pascal code, supports GUS and SB (unfortunately needs EMS), open source, doesn’t work fine under Win9x
DemoVT – resident player (can be used with BASIC demos!), MOD/S3M, GUS/SB
MODOBJ and STMIK are too old, GUSPlay is simple to use but GUS-only, BWSB nags upon exit
32 bit – “are you still complain against 386? we’re going after you!”
Indoor Music System – Cubic Player’ internal engine, plays MOD/S3M/XM/IT, supports GUS/SB/AWE32 native, Windows-compatible, a bit slippy to use, Watcom only
  the MXMPlay fork is compact and fits great for 64k intros, XM/GUS only, PMODE/Watcom, Windows-friendly
MIDAS 1.1.2 – the definite music system, plays MOD/S3M/XM/IT, supports GUS/SB, cross platform (Watcom/DJGPP/Win32/Linux)
JUDAS Sound System – optimized mixer, plays MOD/S3M/XM/IT, supports GUS/SB, Watcom only, doesn’t work under Windows
Useless Module Player - plays MOD/S3M/XM/IT, supports GUS/SB/PC Speaker (yes!), PMODE/EOS/Watcom, also hates Windows
RXMPlay – XM only, compact, GUS/SB/AWE32, PMODE/Watcom, Windows-friendly

## Slide 115
emulators :: virtual machines
don’t use them. Not even VMware. Not even Oracle VM VirtualBox.
since VMs are focused to run newer host systems, they don’t bother to emulate common features being used by DOS high-performance stuff (cycle-accurate VGA emulation, VBE, etc)
Bochs/QEMU is relatively decent, but please refrain from using them as first-class testing environment

## Slide 116
emulators :: dosbox
the easiest and most balanced way to test your DOS stuff :)
emulates DOS environment, can mount host folders as disks, floppy and CD images
vanilla DOSBox builds are games-oriented and feature-limited, doesn’t cycle-accurately emulate VGA well, had trouble with tricky stuff, seldom updates
…fortunately, as it’s open-source, better forks exist, i.e. DOSBox-X:
emulates everything from PC/XT to Pentium Pro/MMX, and even PC-98!
near perfect VGA emulation (still improving but runs 99% of demos great), great SB/GUS support, emulates SVGA (as S3 Trio64) and 3dfx Voodoo well
can boot and run Windows 3.x/95/98 (if you really want it)
works on Windows, Linux and macOS, and even able to run under real MS-DOS :)

## Slide 117
emulators :: pcem
contrary to DOSBox and like other platforms emulators, emulates full PC environment
cycle-exact device emulation (the 8088+GCA configuration runs 8088 MPH almost perfectly)
emulates lots of devices (floppy and hard drives, CGA/EGA/VGA + several SVGA models, SB16/AWE32/GUS/Interwave, 3dfx Voodoo and much more)
easy to adjust configuration – from 8088/4.77MHz to Pentium MMX/II
uses real hardware ROMs (not HLE like DOSBox), you have to find them on the Internet and place in emulator ROM folder
stopped active development in 2021 :( latest version released in Dec ‘20

## Slide 118
sizecoding
art of making audiovisual stuff in extremely tiny executables
(512 bytes or less )

## Slide 119
sizecoding :: why dos?
usually, larger size intros (1k and more) are coded for Windows or Linux, taking advantage of advanced graphics capabilities
in case of 512b or less, the EXE header alone eats about 50-100 bytes and initialization code takes as much as same, if not more!
in contrast, DOS .COM files are just pure header-less executables, and graphics/sound initilaization takes only several dozens bytes
cons: no fancy hardware 3D, 16-bit code by default
on the other hand, accessing i.e. VRAM or playing sound is easier and smaller code-wise than under Windows
some intros even take advantage of high VBE resolutions and modern instruction sets like SSE4/AVX, and everything under DOS! :)
sound is more troublesome, though
  MIDI is easies tto use, following by Covox and PC Speaker

## Slide 120
sizecoding :: tricks
sizecoding.org provides lots of incredibly valuable info about tiny intro tips and tricks
linear modes like 320x200 256 colors are the easiest and fastest to work with
.COM files suits best for sizecoding, and you can even write your intro in a boot sectpr!
during .COM startup, several registers are set to known state, so you can use default values to save some bytes
enable listing output in your assembler and mark the hot spots with long opcodes your code, then prioritize them for size optimizing
use full 16-bit register for simple instructions (dec, inc, add and so on), take a look on 1-byte instructions (movs/stos/xlat/etc.)
use code as floating point constants – can really save a byte or two, if not more :)
even default VGA palette can be useful, esp. if you’re running out of free space

## Slide 121
closing words :: tips & advices
learn from others, don’t hesitate to look into code sources
but at the same time, be creative! restrain from blatantly riping and copying effects, add something from yourself :)
test your production on as much machines/platforms as you can
do not lock out on specific hardware without a reason (like making a Pentium/VESA demo GUS-only)
  yea, Gargaj, I’m talking about you :)
provide a decent video capture, but try to forget about real HW enjoyers :)
don’t be afraid of your first steps, create, release, learn and improve
  everything is evolving iteratively

## Slide 122
Q & A time :)

## Slide 123
….and don’t forget to come to Combined 256b Intro Compo!...
…and other compos @ Demodulation as well :)
…i made a little surprise for you, IBM PC lovers :)

## Slide 124
thanks for reading and watching!
seminar materials (with examples)
https://github.com/wbcbz7/yadm21_seminar
contact:
wbcbz7.at(at)gmail.com
https://t.me/wbcbz7
discord:wbcbz7#3519